## Slide 1
Video Data Collected on R/V Endeavor August 3-18, 2006 David Lyzenga Amanda Dye University of Michigan
SW06 Review Meeting La Jolla, CA Jan 30 - Feb 1, 2007

## Slide 2: SW06 Video Data Collection on R/V Endeavor
Amanda with DVD recorder in lab
video camera installation on bow mast

## Slide 3: Data Collection Details
Cameras were mounted 10.2 meters above the water surface, looking forward at an angle of 45 from the vertical
The angular FOV was approximately 60 for camera 1 and 20 for camera 2
Images from camera 2 are approximately 5 meters on a side
Data was recorded on two DVD recorders at 30 frames per second (480x720 interlaced pixels per frame)
Time code signals from a Horita time code generator were recorded on one of the audio channels, and GPS data from the R/V Endeavor were recorded on the other channel

## Slide 4
Example Wide-Angle Video Data
collected 21:17:47 – 21:19:17 GMT on August 10, 2006

## Slide 5
Example High-Resolution Video Images
four frames selected at 20-second time intervals
while crossing an internal wave on August 9, 2006
(lower panels show corresponding image spectra)

## Slide 6: Data Processing
GPS signals were reconstructed from audio channel recordings and decoded in order to establish time base
Video frames are extracted from the DVD recordings and converted to BMP images using the VirtualDubMod tool (http://sourceforge.net/projects/virtualdubmod)
Alternate scan lines are selected to remove interlacing effects, and image spectra calculated using 2-D FFTs

## Slide 7: Audio Channel (GPS Data) Processing
GPS serial data is distributed at 4800 baud (bits/sec) and recorded on DVD audio channel at 48000 samples/sec
Digital zeros are represented by a positive voltage and ones by a negative voltage
Each character is represented by a (zero) start bit, eight data bits (in reverse order, with most significant bit first), and a stop bit

## Slide 8: Utilization of GPS Data
GPS data consists of four types of NMEA strings (GPGLL, GPVTG, GPZDA, and HEHDT) each transmitted about once per second and one string (GPGGA) transmitted at irregular intervals
GPS time (UT) stored in GPZDA string was correlated with sample number to establish time base for DVD recordings

## Slide 9: Ship Track and Speed
start
stop
Do rapid fluctuations in ship speed indicate internal wave activity? (Ship speed should remain fairly constant relative to water)

## Slide 10: Video Data Processing
For overview purposes, 3 minutes of video data were selected starting at 4 minutes from start of Disk 17B, using one frame per second (frames 7200 to 12600, every 30th frame)
Every other line was selected, and pairs of samples averaged along each line, resulting in 180 360x240-pixel images
Each frame was trimmed horizontally and padded vertically to form 256x256 subsets for FFT processing
2-D FFTs were squared, quadrant-flipped, log transformed, and scaled uniformly to produce a sequence of image spectra

## Slide 11: Video Images 19:39:41 – 19:42:41 GMT on August 9, 2006

## Slide 12
Combined Images and Spectra 19:39:41 – 19:42:41 GMT on August 9, 2006

## Slide 13: Analysis Plans
Surface wave spectral perturbations
Surface currents from 3-D spectra and/or feature tracking
Frequency of wave breaking from wide-angle images
Comparisons with in situ measurements, radar and remote sensing data
Suggested collaborators:
  UW (Henyey) – i.w. displacements, surface currents
  UW (Plant) and Miami (Graber) – near-surface radar, remote sensing (SAR) images